## Slide 1
Collective-Aware In-Switch Telemetry for Distributed AI & HPC Workloads
Detecting synchronization stragglers in AllReduce / Ring-Shift / Gather operations through operation-context-aware telemetry aggregation in programmable data planes (P4).
W1
W2
W3
W4
P4 SWITCH
NETWORK
Department of Computer Science & Engineering · VNIT Nagpur
FINAL YEAR PROJECT · 1ST EVALUATION
Rakshit Singhvi – BT23CSE023
Deev Shah – BT23CSE108
Vraj Borad – BT23CSE119
Tanushree Harish – BT23CSE120
Collective Telemetry

## Slide 2
01 · BACKGROUND
Programmable Data Planes & Network Telemetry
Two building blocks this project rests on, before we get to the problem itself.
PROGRAMMABLE DATA PLANES (P4)
Traditional switches are fixed-function ASICs — the forwarding logic is baked into the hardware and cannot be changed
P4 (Programming Protocol-independent Packet Processors) lets us program how a switch parses, matches, and processes packets — same chip, a custom pipeline
Core building blocks: Parser → Match-Action Tables → Stateful Registers → Deparser, arranged into a fixed number of pipeline stages
Hardware limits: no native division / floating point; limited SRAM, TCAM and stages per switch
NETWORK TELEMETRY & INT
Telemetry = real-time visibility into what's happening inside the network (delay, queue occupancy, drops) rather than inferring it from the endpoints
In-Band Network Telemetry (INT): the packet itself carries instructions; every switch on its path appends its own measurements directly into the packet header
Gives fine-grained, per-hop, real-time visibility with no separate monitoring channel
Overhead concern: telemetry added to every packet costs bandwidth — motivating selective, event-driven telemetry designs
PACKET
SW1
+ metadata
SW2
+ metadata
COLLECTOR
(reads full path)
We prototype on BMv2 — the standard P4 software reference switch
02

## Slide 3
02 · BACKGROUND
Collective Communication Operations
Distributed ML training and HPC jobs coordinate workers through a handful of standard collective patterns. Each defines a different way data moves between participants — but all of them are barrier-synchronized: every worker must finish before the step is considered complete.
AllReduce
Aggregates values (e.g. gradients) across all workers and returns the combined result to every worker.
AllGather
Each worker collects data from every other worker, so all workers end up holding the full combined set.
ReduceScatter
Combines data across workers, then splits the result so each worker receives only its own portion.
All-to-All
Every worker sends a distinct chunk of data to every other worker — a fully personalized exchange.
Ring-Shift / Ring-based
Workers are arranged in a logical ring; each passes data to its neighbor in sequence, forming a pipeline.
Gather
Partial results from many workers are collected into a single worker (the root).
Broadcast
One worker's data is sent out to all other participating workers.
This project focuses on AllReduce, Ring-Shift, and Gather as representative barrier-synchronized patterns
03

## Slide 4
03 · INTRODUCTION
Application Domain: Barrier-Synchronized Collectives
Distributed machine-learning training and HPC clusters rely on barrier-synchronized collective communication — operations where every participating worker must finish exchanging data before computation can resume.
“All workers must complete their exchange before the next compute step begins — the slowest link sets the pace.”
This project sits at the intersection of distributed-systems networking and programmable data planes: using P4-based switches to reason about collective operations, not just individual packets or flows.
BARRIER SYNCHRONIZATION
W1
W2
W3 (lag)
W4
barrier
AllReduce aggregates gradients across all workers each training step. Ring-Shift passes data around a logical ring of workers. Gather collects partial results from many workers to one.
04

## Slide 5
04 · MOTIVATION
Why This Problem Matters
1
The Cost of One Straggler
In a barrier-synchronized operation, one delayed worker extends the completion time of the entire collective — and therefore the whole training step. Completion time = slowest participant; a single delayed worker can stall N synchronized peers in every AllReduce round.
2
Transient Delays Become Job-Level Stragglers
A brief network hiccup affecting a single flow can silently propagate into extended distributed-job execution time — the delay is invisible until the whole step is late.
3
Telemetry Today Is Blind to This Dependency
In-Band Network Telemetry (INT) observes packets and flows independently. Per-packet — yes. Per-flow — yes. Per-collective-operation — no.
This gap between network-level observation and application-level synchronization semantics motivates a collective-aware design
05

## Slide 6
05 · CHALLENGES
Key Challenges
01
Flow-centric abstractions
Prior systems (INT-LLPP, STRAGFLOW) reduce overhead or catch delays, but still reason per-flow — none correlate flows sharing a collective operation.
02
No shared operation context
Switches see independent 5-tuples; associating packets from different workers with the same synchronization step needs a lightweight shim.
03
P4 hardware arithmetic limits
P4 hardware targets (including our BMv2 prototype) cannot do division / floating point — skew, thresholds and priorities must use only stateful registers and match-action tables.
04
Limited stages & memory
Maintaining per-operation min/max timestamps and context state must fit within a small number of pipeline stages and SRAM/TCAM blocks.
05
Overhead vs. accuracy tradeoff
As seen across all three reference papers, tighter monitoring accuracy generally costs more control/forwarding overhead — a balance our design must strike too.
06
Threshold design under dynamic skew
The operator-defined skew threshold δt must stay meaningful as network conditions, topology and traffic patterns change at runtime.
06

## Slide 7
06 · SCOPE
Problem Statement
EXISTING PROBLEM
Existing network telemetry observes packets and flows independently, providing limited visibility into the performance of an entire collective operation — so a single lagging participant in an AllReduce, Ring-Shift, or Gather cannot be identified in-network.
PROPOSED PROBLEM
Design an in-switch, collective-aware telemetry aggregation framework that associates participating flows with a shared operation context, aggregates their network-level timing information, detects abnormal synchronization skew, and reports relevant network state only when a potential collective straggler is observed.
There remains a gap between network-level runtime observation and collective-level synchronization semantics
07

## Slide 8
06 · SCOPE
Goal & Expected Outcomes
Design and implement an in-switch, collective-aware telemetry aggregation framework in programmable data planes that associates flows via a shared context identifier, aggregates timestamps in switch memory, and triggers telemetry only on abnormal skew.
EXPECTED OUTCOMES
PROPOSED
Context-Shim Header
Lightweight header design mapping packets to a shared operation context.
PROPOSED
P4 Skew Prototype
Computes intra-operation skew (δt) via stateful registers on the data plane.
PROPOSED
In-Switch Aggregation
Aggregates min/max arrival timestamps directly in switch memory.
PROPOSED
Event-Driven Reporting
Straggler-triggered reporting instead of per-packet telemetry.
PROPOSED
Lower Overhead
Reduced control/telemetry overhead vs. per-flow INT baselines.
08

## Slide 9
07 · LITERATURE SURVEY — RELATED WORK 1 OF 3
INT-LLPP — Network-Wide Telemetry Path Planning
Zhang, H. Zhang, Dai, Zeng, Wang & Liao — Computer Communications 236 (2025)
KEY IDEA
One shared set of probes per switch collects all telemetry items — avoids repeated probing for each telemetry task
Probe Path Generation (PPG): plans probe paths for full network coverage while minimizing forwarding overhead
Simulated Annealing Maximum Latency Setting (SAMLS): balances telemetry latency against control overhead
RESULTS (vs. INT-path / IntOpt / NetView)
Control overhead reduced by over 50%
Forwarding overhead reduced by 5% – 10%
Telemetry latency reduced by 30% – 40%
GAP VS. OUR PROBLEM
Optimizes what and how telemetry is collected across the network — but each probe path still reasons about individual flows. There is no notion of multiple flows belonging to one synchronized collective operation.
09

## Slide 10
07 · LITERATURE SURVEY — RELATED WORK 2 OF 3
P4InfoSen-INT — Information-Sensitive Telemetry
Xu, Lu & Zhu — Information-Sensitive In-band Network Telemetry in P4-based Programmable Data Plane
KEY IDEA
Each switch locally decides which telemetry field to insert, based on its information content: I = −log₂ P(value)
Priority Mapping Table (PMT) built from match-action tables ranks telemetry types (original paper targets Tofino hardware)
Polling-based INT + Prioritized INT operate together; sampling rate adapts to real-time bandwidth usage
SCALABILITY (Table Merging + Table Entry Merging)
Pipeline stage usage reduced from 9 stages to 5 stages
Outperforms PINT and AINT baselines on the overhead / accuracy tradeoff
GAP VS. OUR PROBLEM
Reduces redundant per-flow reporting by prioritizing the most informative field — but each flow is still assessed independently. No mechanism correlates telemetry across flows of a shared operation.
10

## Slide 11
07 · LITERATURE SURVEY — RELATED WORK 3 OF 3
STRAGFLOW — Data-Plane Straggler Detection
Maulana, Mostafaei & Meratnia — IFIP Networking 2025, Limassol, Cyprus
KEY IDEA
Uses deq_timedelta, a queueing-delay metadata field available on Tofino hardware, in the egress pipeline
A packet is a straggler if its delay exceeds the highest delay previously seen for that same flow
A Count-Min Sketch "Straggler Counter" tracks per-flow straggler counts with low memory; reports sent to the control plane via digest once a threshold is hit
RESULTS (CAIDA traces, PIAS vs. FIFO)
PIAS scheduling reduces detected stragglers by up to 49% vs. FIFO
Resource-light on their Tofino testbed: 0% TCAM, 0% stateful ALUs, 6 of 12 pipeline stages
GAP VS. OUR PROBLEM
"Straggler" is defined per-flow against its own past behavior — not against sibling flows participating in the same collective operation.
11

## Slide 12
07 · LITERATURE SURVEY
The Gap We Target
Work | Focus | Flow-aware | In-switch | Collective-aware
INT-LLPP (2025) | Network-wide INT path planning | ✓ | ✓ | ✗
P4InfoSen-INT | Information-sensitive telemetry | ✓ | ✓ | ✗
STRAGFLOW (2025) | Per-flow straggler detection | ✓ | ✓ | ✗
(proposed) | Collective-aware telemetry aggregation | ✓ | ✓ | ✓
THE GAP
None of the three correlate multiple flows belonging to a single barrier-synchronized collective operation. Our design introduces a shared operation-context identifier so switches can reason across flows, not just within one.
12

## Slide 13
08 · SYSTEM DESIGN
Proposed Architecture
PROPOSED
W1
W2
W3
W4
DISTRIBUTED WORKERS
Collective Packets (context-shim tagged)
P4 SWITCH PIPELINE
Context-Shim Parsing
Operation-Context Lookup
Timestamp Update (min/max)
Skew Calculation (δt)
Threshold Check (δt > θ)
NORMAL
Forward packet
STRAGGLER
Clone / Digest
CONTROL PLANE
TELEMETRY ANALYSIS
Only anomalous collective states are cloned to the control plane — normal traffic is forwarded with no added overhead.
13

## Slide 14
08 · SYSTEM DESIGN
Inside the P4 Switch
PROPOSED
1 · Parse
Extract Operation-Context ID and Participant ID from the context-shim header
2 · Lookup
Use the Context ID to access stateful registers for this collective operation
3 · Update
Record arrival timestamp:
t_fast = min(t_fast, t)
t_slow = max(t_slow, t)
4 · Calculate
δt = t_slow − t_fast
(no division/floats — pure register arithmetic)
5 · Decide
δt ≤ θ → Normal → Forward
δt > θ → Straggler → Report
IMPORTANT WORDING
Avoid: “Guaranteed straggler identification.” Use: “Potential collective straggler detection based on abnormal synchronization skew.”
14

## Slide 15
09 · IMPLEMENTATION
Dataset & Implementation Details
PROPOSED / PLANNED
TARGET PLATFORM
P4 programmable data plane — implemented and evaluated entirely on BMv2, the standard P4 software reference switch
All prototyping stays within BMv2 + Mininet
PLANNED DATASET / TRAFFIC
Synthetic collective-communication traffic emulating AllReduce / Ring-Shift / Gather
Mininet-based emulated testbed with multiple switches
Controlled injected network delay on a subset of participants to emulate stragglers
Reference traffic patterns informed by traces used in STRAGFLOW (CAIDA)
PLANNED METRICS
Detection latency of the lagging participant
Telemetry / control overhead vs. per-flow INT baselines (INT-LLPP, P4InfoSen-INT)
Accuracy of intra-operation skew (δt) estimation
Status: implementation not yet started — see Early Progress for current hands-on work
15

## Slide 16
10 · TIMELINE & EARLY PROGRESS
Six-Month Plan & Where We Are Now
MONTH 1
Literature Review + Problem Formulation
DONE
MONTH 2
Early P4 Experimentation (BMv2)
CURRENT
MONTH 3
Context-Shim + Skew Prototype
MONTH 4
Mininet Testbed + Control Plane
MONTH 5
Extended BMv2 Evaluation & Scaling
MONTH 6
Final Evaluation vs. Baselines
EARLY EXPERIMENTATION WITH P4
We have started hands-on experimentation with P4 — writing and running basic programs on a software switch (BMv2) to build familiarity with the language, the packet-processing pipeline, and stateful register operations before implementing the full context-shim design.
Planned next: BMv2 P4 program output, switch CLI / table state, and test-traffic results from initial experiments
16

## Slide 17
SUMMARY
From Flow-Centric to Collective-Aware Telemetry
SUMMARY
We propose an in-switch, operation-context-aware telemetry framework that correlates flows of the same barrier-synchronized collective, aggregates timing state directly in P4 switch memory, and reports only when a genuine straggler emerges — closing a gap left open by INT-LLPP, P4InfoSen-INT, and STRAGFLOW.
NEXT MILESTONE
Evaluation 2 — working P4 prototype with skew-based straggler reporting.
DESIGN PRINCIPLE
Collect → Aggregate → Report
instead of per-packet Collect → Report cycles.
Thank You
Questions & Discussion
17